Continuous Functions
All functions below be f: setR toward setR unless otherwise stated.
Each elementary function is continuous on its domain. Addition, subtraction, multiplication, division by nonzero and composition of continuous functions give continuous functions.
1. f(lnx) is continuous for all x>0. Does f(x) be continuous for all x?
2. a) Both f(x-1)+7f(x+1) and f(x+1)+7f(x-1) be continuous. Is f(x) continuous?
b) For every real a>1, the function f(x)+f(ax) be continuous, prove that f is continuous.
Intermediate value theorem. If the real-valued function f is continuous on the closed interval [a, b] and k is some number between f(a) and f(b), then there is some number c in [a, b] such that f(c) = k.
3. Let f(x) be continuous on [a, b] and f(a)f(b)le 0 . Prove that f(x) has a root on [a, b].
4. Prove that some chord cut from a circle exactly 1/3 of its area.
5. 97903 f(x + 1)f(x) + f(x + 1) + 1 = 0 ~~forall x . Prove that f is discontinuous.
6. 116994 Given x_{1}, x_{2}, ..., x_n in [0, 2] , prove that abs{x – x_1} + abs{x – x_2} + ... + abs{x – x_n} = n for some x in [0, 2] .
7. 35573 Let f(x) be continuous on [0, 100] and f(0)=f(100). Prove that exists a in [0,~99]: f(a)=f(a+1) .
Extreme value theorem. If the real-valued function f is continuous on the closed interval [a,b], then the function attains its maximum, i.e. there exists  c in [a, b] with  f(c) ge f(x) ~~forall x in [a,b] . The same is true of the minimum of f.
8. 111264 Let f be continuous and f(x^2)-f^2(x) ge 0.25 ~~forall x . Does that imply f has an extremum point?
9. 35771 Does there exist a continious function f: setR toward setR that attains each real value exactly 3 times?
10. Prove that forall a_1, b_1, a_2, b_2, ..., a_n, b_n in setR the equation a_1"sin"x +b_1"cos"x + a_2"sin"2x +b_2"cos"2x + ... + a_n"sin"nx +b_n"cos"nx = 0 has a solution.
11. RNO1993. Given f: setR_pos rightarrow setR_pos such that f(x^y)=f(x)^{f(y)}~~forall x,y in setR_pos ,
a) find all such continuous functions, b) find all such functions.
### Credit problems
CF1. (IMC6.2.2) Find all functions f: setR rightarrow setR such that for any real numbers a<b , the image f([a,b]) is a closed interval of length b-a .
CF2. (IMC8.1.1) Find all continuous functions f: setR rightarrow setR such that f(x+q)-f(x) in setQ ~~forall x in setR, q in setQ .
www.ashap.info/Uroki/eng/NYUAD18/index.html